## Slide 1: COMPUTER ARITHMETIC

## Slide 2
Introduction
CPU consists of
control unit
registers
arithmetic and logic unit (ALU)
instruction execution unit
interconnections among these components
Representations of numbers (binary format) and techniques for implementing arithmetic operations (add, subtract, multiply, divide) are functions of ALU.
These two considerations apply to integers and floating-point arithmetic.

## Slide 3
Arithmetic and Logic Unit (ALU)
ALU is that part of computer that actually performs arithmetic and logical operations on data.
All of other elements of computer system (control unit, registers, memory, I/O) are there mainly to bring data into ALU for it to process and then to take results back out.
An ALU are based on use of simple digital devices that can store binary digits and perform simple Boolean logic operations.

## Slide 4
Arithmetic and Logic Unit (ALU)
Figure shows how ALU is interconnected with rest of processor:
Data are presented to ALU in registers and results of an operation are stored in registers.
These registers are temporary storage locations within processor that are controlled by signal paths to ALU.
ALU may set flags as result of an operation. (e.g. overflow flag is set to 1, if length of a computation exceeds length of register into which it is to be stored).
Control unit provides signals that control operation of ALU and movement of data into and out of ALU.

## Slide 5
Integer Representation
In binary number systems, only binary digits (0 and 1) may be used to represent numbers.
Positive numbers are stored in binary, representation is straightforward:
  00000000 = 0
  00000001 = 1
  00101001 = 41
  10000000 = 128
  11111111 = 255

## Slide 6
Integer Representation
00101001 = 41
0 0 1 0 1 0 0 1
128 64 32 16 8 4 2 1
= 1 + 8 + 32
= 41

## Slide 7
Integer Representation
67 = ?
128 64 32 16 8 4 2 1
0
1
64 +
1
2 = 66
1
+ 1 = 67
0 0 0 0
01000011

## Slide 8
Sign-Magnitude Representation
Leftmost bit is sign bit:
  0 for positive
  1 for negative
Remaining bits are magnitude.
Example:
  +18 = 00010010
  -18 = 10010010
Drawbacks:
  Need to consider both sign and magnitude in arithmetic.
  There are two representations of 0:
    +010=00000000
    -010 =10000000
  Sign-magnitude representation is rarely used in implementing integer portion of ALU.

## Slide 9
Most common scheme is twos complement representations.
Twos complement representation:
Leftmost bit still indicates sign:
  0 for positive
  1 for negative
Positive numbers are exactly same as sign-magnitude.
  +18 = 00010010
Zero is only all zeros (positive).
  0 = 00000000
Negative numbers are found by taking twos complement.
  Take complement of positive version.
  Add 1.
Twos Complement Representation

## Slide 10
Twos Complement Representation
Getting -55
  Start with +55
Twos complement examples
(with 8 bit numbers)
-128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
An eight position twos compliments value box
1
1
1
1
32 + 16 + 4 + 2+1 =55
0 0 0
1
55 = 00110111

## Slide 11
Twos Complement Representation
Twos complement examples
(Getting -55)
+55 = 00110111
Compliment that 
11001000
Add 1 
00000001
+
11001001
Result is –55 
11001001

## Slide 12
Twos Complement Representation
Twos complement examples
(with 8 bit numbers)
-128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
An eight position twos compliment value box
1 1 0 0 1 0 0 1
-128 + 64 + 8 + 1 = -55
Check -55 = 11001001

## Slide 13
Twos Complement Representation
Twos complement examples
Negating -55
Compliment that 
00110110
Add 1 
00000001
+
00110111
Result is +55 
00110111
Start with -55 = 11001001

## Slide 14
Range of numbers:
8 bit twos compliment
  +127 = 01111111 = 27 -1
  -128 = 10000000 = -27
16 bit twos compliment
  +32,767 = 011111111 11111111 = 215 – 1
  -32,768 = 100000000 00000000 = -215
Twos Complement Representation

## Slide 15
Take an n-bit integer and store it in m bits, where m>n.
Move sign bit to new leftmost position.
  In sign-magnitude notation, fill in with zeros.
    Examples (8 bit → 16 bit)
      +18: 00010010 → 0000000000010010
      -18: 11101110 → 1000000001101110
  In twos complement notation, fill in with copies of sign bit, called sign extension.
    Examples (8 bit → 16 bit)
      +18: 00010010 → 0000000000010010
      -18: 11101110 → 1111111111101110
Converting between Different Bit Lengths

## Slide 16
On any addition, results may be larger than can be held in word size being used. This condition is called overflow.
When overflow occurs, ALU must signal this fact so that no attempt is made to use result.
To detect overflow, following rule is observed:
If two numbers are added and they are both positive or negative then overflow occurs if and only if result has opposite sign.
Integer Arithmetic

## Slide 17
Perform normal binary addition.
Monitor sign bit for overflow.
In some instances, there is a carry bit beyond end of word (indicated as red), which is ignored.
Integer Arithmetic: Addition in twos complement representation

## Slide 18
Addition Examples
1001 = -7 +0101 = 5 1110 = -2
(a) (-7) + (+5)
 | -8 | 4 | 2 | 1
-7 | 1 | 0 | 0 | 1
5 | 0 | 1 | 0 | 1
-2 | 1 | 1 | 1 | 0
Integer Arithmetic: Addition in twos complement representation

## Slide 19
Addition Examples
1100 = -4 +0100 = 4 10000 = 0
(b) (-4) + (+4)
 | -8 | 4 | 2 | 1
4 | 1 | 1 | 0 | 0
+4 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0
×
Carry bit
Integer Arithmetic: Addition in twos complement representation

## Slide 20
Addition Examples
1100 = -4 +1111 = -1 11011 = -5
(c) (-4) + (-1)
 | -8 | 4 | 2 | 1
- 4 | 1 | 1 | 0 | 0
- 1 | 1 | 1 | 1 | 1
- 5 | 1 | 0 | 1 | 1
×
Carry bit
Integer Arithmetic: Addition in twos complement representation

## Slide 21
Addition Examples
0101 = 5 +0100 = 4 1001 = -7 ×
(d) (+5) + (+4)
 | -8 | 4 | 2 | 1
5 | 0 | 1 | 0 | 1
4 | 0 | 1 | 0 | 0
7 | 1 | 0 | 0 | 1
Overflow
Integer Arithmetic: Addition in twos complement representation

## Slide 22
Integer Arithmetic: Addition in twos complement representation
Addition Examples
1001 = -7 +1010 = -6 10011 = 3 ×
(e) (-7) + (-6)
 | -8 | 4 | 2 | 1
-7 | 1 | 0 | 0 | 1
-6 | 1 | 0 | 1 | 0
3 | 0 | 0 | 1 | 1
Overflow
×
Carry bit

## Slide 23
Take two compliment of subtrahend and add to minuend.
  a - b = a + (-b)
So we only need addition and complement circuits.
A carry bit beyond end of word is indicated as red, which is ignored.
Integer Arithmetic: Subtraction in twos complement representation

## Slide 24
Integer Arithmetic: Subtraction in twos complement representation
Subtraction Examples
0010 = 2 +1001 = -7 1011 = -5
(a) 2 – 7  2 + (-7)
2=0010
7=0111
To obtain -7
complement 7 and add 1
1000
+0001
1001

## Slide 25
Integer Arithmetic: Subtraction in twos complement representation
Subtraction Examples
0101 = 5 +1110 = -2 10011 = 3
(b) 5 – 2  5 + (-2)
5=0101
2=0010
To obtain -2
complement 2 and add 1
1101
+0001
1110
×
Ans: 0011
Carry bit

## Slide 26
Integer Arithmetic: Subtraction in twos complement representation
Subtraction Examples
0111 = 7 +0111 = 7 1110 = -2 !!!
(e) 7 – (-7)  7 + (7)
7 = 0111
Overflow

## Slide 27
Integer Arithmetic: Subtraction in twos complement representation
0010 = 2 +1001 =-7 1011 =-5 (a) M=2=0010 S =7=0111 -S= 1001 | 0101 = 5 +1110 =-2 10011 = 3 (b) M=5=0101 S =2=0010 -S= 1110
1011 =-5 +1110 =-2 11001 =-7 (c) M=-5=1011 S =2 =0010 -S= 1110 | 0101 = 5 +0010 = 2 0111 = 7 (d) M=5 =0101 S =-2=1110 -S= 0010
0111 = 7 +0111 = 7 1110 =Overflow (e) M=7 =0111 S =-7=1001 -S= 0111 | 1010 =-6 +1100 =-4 10110 = Overflow (f) M=-6=1010 S = 4 =0100 -S= 1100

## Slide 28
Figure suggest data paths and hardware elements needed to accomplish addition and subtraction.
Integer Arithmetic: Addition and Subtraction
Central element is binary adder, which is presented two numbers for addition and produces a sum and an overflow indication.
For addition, two numbers are presented from two registers.
Result may be stored in one of these registers or in a third.
Overflow indication is stored in a 1-bit overflow flag.
  0 = no overflow
  1 = overflow
For subtraction, subtrahend (B register) is passed through a twos complementer so that its twos complement is presented to adder.