## Slide 1: LOGIC GATES
Formal logic: In formal logic, a statement (proposition) is a declarative sentence that is either
true(1) or false (0).
It is easier to communicate with computers using formal logic.
• Boolean variable: Takes only two values – either
true (1) or false (0).
They are used as basic units of formal logic.

## Slide 2: Boolean function and logic diagram
• Boolean function: Mapping from Boolean variables to a Boolean value.
• Truth table:
  Represents relationship between a Boolean function and its binary variables.
  It enumerates all possible combinations of arguments and the corresponding function values.

## Slide 3: Boolean function and logic diagram
• Boolean algebra: Deals with binary variables and logic operations operating on those variables.
• Logic diagram: Composed of graphic symbols for logic gates. A simple circuit sketch that represents inputs and outputs of Boolean functions.

## Slide 4: Gates
Refer to the hardware to implement Boolean operators.
The most basic gates are

## Slide 5: Boolean function and truth table

## Slide 6: BASIC IDENTITIES OF BOOLEAN ALGEBRA
Postulate 1 (Definition): A Boolean algebra is a closed algebraic system containing a set K of two or more elements and the two operators · and + which refer to logical AND and logical OR

## Slide 7: Basic Identities of Boolean Algebra (Existence of 1 and 0 element)
x + 0 = x
x · 0 = 0
x + 1 = 1
x · 1 = 1
(Table 1-1)

## Slide 8: Basic Identities of Boolean Algebra (Existence of complement)
(5) x + x = x
(6) x · x = x
(7) x + x’ = x
(8) x · x’ = 0

## Slide 9: Basic Identities of Boolean Algebra (Commutativity):
(9) x + y = y + x
(10) xy = yx

## Slide 10: Basic Identities of Boolean Algebra (Associativity):
(11) x + ( y + z ) = ( x + y ) + z
(12) x (yz) = (xy) z

## Slide 11: Basic Identities of Boolean Algebra (Distributivity):
(13) x ( y + z ) = xy + xz
(14) x + yz = ( x + y )( x + z)

## Slide 12: Basic Identities of Boolean Algebra (DeMorgan’s Theorem)
(15) ( x + y )’ = x’ y’
(16) ( xy )’ = x’ + y’

## Slide 13: Basic Identities of Boolean Algebra (Involution)
(17) (x’)’ = x

## Slide 14: Function Minimization using Boolean Algebra
Examples:
(a) a + ab = a(1+b)=a
(b) a(a + b) = a.a +ab=a+ab=a(1+b)=a.
(c) a + a'b = (a + a')(a + b)=1(a + b) =a+b
(d) a(a' + b) = a. a' +ab=0+ab=ab

## Slide 15: Try
F = abc + abc’ + a’c

## Slide 16: The other type of question
Show that;
1- ab + ab' = a
2- (a + b)(a + b') = a
1- ab + ab' = a(b+b') = a.1=a
2- (a + b)(a + b') = a.a +a.b' +a.b+b.b'
= a + a.b' +a.b + 0
= a + a.(b' +b) + 0
= a + a.1 + 0
= a + a = a

## Slide 17: More Examples
Show that;
(a) ab + ab'c = ab + ac
(b) (a + b)(a + b' + c) = a + bc
  (a) ab + ab'c = a(b + b'c)
  = a((b+b').(b+c))=a(b+c)=ab+ac
(b) (a + b)(a + b' + c)
= (a.a + a.b' + a.c + ab +b.b' +bc)
= …

## Slide 18: DeMorgan's Theorem
(a) (a + b)' = a'b'
(b) (ab)' = a' + b'
Generalized DeMorgan's Theorem
(a) (a + b + … z)' = a'b' … z'
(b) (a.b … z)' = a' + b' + … z‘

## Slide 19: DeMorgan's Theorem
F = ab + c’d’
F’ = ??
F = ab + c’d’ + b’d
F’ = ??

## Slide 20: DeMorgan's Theorem
Show that: (a + b.c)' = a'.b' + a'.c'

## Slide 21: More DeMorgan's example
Show that: (a(b + z(x + a')))' =a' + b' (z' + x')
  (a(b + z(x + a')))' = a' + (b + z(x + a'))'
  = a' + b' (z(x + a'))'
  = a' + b' (z' + (x + a')')
  = a' + b' (z' + x'(a')')
  = a' + b' (z' + x'a)
  =a‘+b' z' + b'x'a
  =(a‘+ b'x'a) + b' z'
  =(a‘+ b'x‘)(a +a‘) + b' z'
  = a‘+ b'x‘+ b' z‘
  = a' + b' (z' + x')

## Slide 22: More Examples
(a(b + c) + a'b)'=b'(a' + c')
ab + a'c + bc = ab + a'c
(a + b)(a' + c)(b + c) = (a + b)(a' + c)

## Slide 23: DeMorgan’s Theorems

## Slide 24: DeMorgan’s Theorems
DeMorgan’s Theorems are two additional simplification techniques that can be used to simplify Boolean expressions. Again, the simpler the Boolean expression, the simpler the resulting logic.
A  B  A B A B  A  B
2

## Slide 25: DeMorgan’s Theorem #1
A B  A  B
Proof
A  B
A B
A B
A B
A B
A
B
A
B
A  B
A | B | A B | A B
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
A | B | A | B | A  B
0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0
The truth-tables are equal; therefore, the Boolean equations must be equal.

## Slide 26: DeMorgan’s Theorem #2
A  B  A  B
Proof
A B
A  B
A  B
A B
A
B
A
B
A B
A  B
A | B | A  B | A  B
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
A | B | A | B | A B
0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0
The truth-tables are equal; therefore, the Boolean equations must be equal.

## Slide 27: Summary
Boolean & DeMorgan’s Theorems
Commutative Law
X  Y  Z  X  Y  Z XY  Z  XY  XZ
X  Y  Y  X X  Y  Y  X
XYZ  XYZ
Associative Law
Distributive Law
1) X  0  0
2) X  1  X
3) X  X  X
4) X  X  0
5) X  0  X
6) X  1  1
7) X  X  X 8) X  X  1
10A)
10B)
11A)
11B)
12A)
12B)
13A)
13B)
X  XY  X  Y
X  YW  Z  XW  XZ  YW  YZ X  XY  X  Y
9) X  X
13C)
13D)
X  XY  X  Y
X  XY  X  Y
Consensus Theorem
14A)
14B)
X Y  X  Y
X  Y  X Y
DeMorgan’s
5

## Slide 28: DeMorgan Shortcut
BREAK THE LINE, CHANGE THE SIGN
Break the LINE over the two variables,
and change the SIGN directly under the line.
A B  A  B
For Theorem #14A, break the line, and change the AND function to an OR function. Be sure to keep the lines over the variables.
A  B  A B
For Theorem #14B, break the line, and change the OR function to an AND function. Be sure to keep the lines over the variables.

## Slide 29: DeMorgan’s: Example #1
Example
Simplify the following Boolean expression and note the Boolean or DeMorgan’s theorem used at each step. Put the answer in SOP form.
F  ( X  Y)  ( Y  Z)
1

## Slide 30: DeMorgan’s: Example #1
Example
Simplify the following Boolean expression and note the Boolean or DeMorgan’s theorem used at each step. Put the answer in SOP form.
Solution
F  ( X  Y)  ( Y  Z)
1
F  ( X  Y)  ( Y  Z)
F  ( X  Y)  ( Y  Z)
1
1
; Theorem #14A
F  ( X  Y)  ( Y  Z)
1
; Theorem #9 & #14B
; Theorem #9
F  XY  YZ
F  ( X  Y)  ( Y  Z)
1
1
; Rewritten without AND symbols and parentheses
8

## Slide 31: DeMorgan’s: Example #2
So, where would such an odd Boolean expression come from? Take a look at the VERY poorly designed logic circuit shown below. If you were to analyze this circuit to determine the output function F2, you would obtain the results shown.
X
Y
XY
XY
X
(X  Z)(XY)
2
F  ( X  Z)(XY)
Z
X  Z
Example
Simplify the output function F2. Be sure to note the Boolean or DeMorgan’s theorem used at each step. Put the answer in SOP form.

## Slide 32: DeMorgan’s: Example #2
; Theorem #14A
; Theorem #9
; Theorem #14B
Solution
F  (X  Z)(XY)
2
F  (X  Z)  (XY)
2
F  (X  Z)  (XY)
2
F  (X Z)  (XY)
2
F  (X Z)  (XY)
2
F  X Z  X Y
2
; Theorem #9
; Rewritten without AND symbols