## Slide 1: Installation, Repair, Servicing & Maintenance concepts

## Slide 2: The Concepts
The effective & efficient working of a system depends on the following four features:
Maintenance
Servicing
Trouble shooting
Repair

## Slide 3: Maintenance
Maintenance includes both hardware & software in it.
Maintenance is a continuous process.
Hardware maintenance includes cleaning dust, maintaining constant voltage, etc.
Software maintenance includes reinstallation, upgradation & removal of different softwares.

## Slide 4: Servicing
Servicing is mainly associated with hardware equipment.
Servicing includes checkups, repairs and updation of all physical components.
Service provider should have proper knowledge about various components and their installation procedures.

## Slide 5: Servicing steps
Uninstall all physical components starting from power connections to internal motherboard connections.
Clean dust from the components.
Perform a visual check or electronic check as required.
Reinstall all components carefully and properly.

## Slide 6: Servicing steps
Check for loose wiring or crack cables.
Check if any jumper is missing, if required replace it with a new one.
Check for physical damages of peripherals and replace them if needed.
Tighten all external connections.
Switch on the power supply and observe.

## Slide 7: Troubleshooting
Troubleshooting is a form of problem solving, often applied to repair failed products or processes on a machine or a system.
The detection and removal of faults in the computer system can also be termed as troubleshooting.
If a problem is detected in a system, it is to be sorted out immediately.
Troubleshooting is of two types :
    Hardware troubleshooting.
    Software troubleshooting.

## Slide 8: Repairing Concepts
Repairing means to rectify the problem in the hardware or software.
While finding or analyzing the faults, it can be decided which hardware or software can be repaired.
Repairing may also include replacement of a component.
It is an essential part of troubleshooting.

## Slide 9: Repair Maintenance policy
Repair of components may result into adding up of cost and delay in operations.
Some failures occur because of repairs, it is called repair generated failures.
Repairs are termed as corrective maintenance.
Corrective maintenance is done when a fault occurs.

## Slide 10: Repair generated failures
These failures depend on the performance of the technician.
The technician during repairing process may leave some loose connections, wrong connections or some broken pins / broken wires.
These can be avoided if the technician rechecks/revise the work done.

## Slide 11: Maintenance
Maintenance is a process which starts with installation of the system and runs through out the life of it.
Maintenance includes both…
  Hardware maintenance.
  Software maintenance.

## Slide 12: Software Maintenance
Software maintenance includes updating, enhancements, changes, repair and replacements.
Altered environment or changed conditions may result in software maintenance.

## Slide 13: Hardware Maintenance
It includes proper cleaning, servicing, repairing or replacing components of the computer.
The following are the two types of maintenance methods used to keep the hardware intact :
  Preventive maintenance.
  Corrective maintenance.

## Slide 14: Preventive Maintenance
Preventive maintenance means maintenance through preventions.
Careful handling of the computer enhances the life of the system and is called preventive maintenance.
Preventive maintenance can be done by taking some general precautions and some special precautions.

## Slide 15: General Precautions
Ensure all peripherals are switched off before the main power is switched off.
Remove all CD’s and USB drives from the computer before switching off the system.
Do not switch off the system when activity LED in hard disk drive glows.
Store CDs and USB drives in clean and cool place where electromagnetic interference is absent.

## Slide 16: …General Precautions
Do not obstruct air circulation to the computer site.
Do not eat or drink while working on the computer system
When not in use, use dust covers for monitor, printer, etc.

## Slide 17: Special Precautions
Do not apply force on key switches.
Do not rest hands on the keyboard.
Do not play with the keyboard after switching off the power.
Cable at keyboard end should not be subjected to high stress.
Do not use rough materials to clean the components of the system.

## Slide 18: …Special Precautions
Use quality ribbon or ink to avoid damage to print head.
The internal parts of printer like stepper motor, print head, etc. should be cleaned properly periodically.
Switch off power before plugging and removing a cable, or inserting and removing a PCB.

## Slide 19: Preventive Maintenance
The position where the system is kept should be dry and away from direct sunlight or rain.
Ensure the hard disk is backed up properly.
Remove dust from circuit boards using air blower.
Run the diagnostic software periodically.

## Slide 20: Corrective Maintenance
It refers to the maintenance procedures that are adopted when any error occurs in the system.
It is contrary to preventive maintenance.
It starts when a failure or crash occurs in the system.
It includes repair and troubleshooting techniques.

## Slide 21: Corrective maintenance steps
In case of failure general troubleshooting concepts should be performed first.
If problem remains, locate the fault using different tools or diagnostic softwares.
Once fault is determined, troubleshoot or replace the component, as required.

## Slide 22: Corrective maintenance tools
Various tools that can be used during corrective maintenance are Data recovery tools from operating system, third party data recovery tools, virus vaccines, etc.
Though preventive maintenance is better yet there are times that corrective maintenance is used due to unseen factors leading to sudden failures.

## Slide 23: Mean time between failure
Mean time between failure(MTBF) is the statistically derived average length of time for which a system component operates before failing.
It is expressed in thousands or tens of thousands of hours which is known as Power ON Hours(POH).
It is a practical indication of components reliability.

## Slide 24: …MTBF
MTBF rating is intended to be used along with the service life of the component.
It can be measured using statistical methods and any measurement will be subject to statistical variation.
The degree of variation depends on the number of components included in the sample used in measurement.

## Slide 25: Mean time to repair(MTTR)
MTTR is amount of time between when something breaks and when it has been repaired.
MTTR represents the total amount of time that the device was unable to provide service.
MTTR numbers are calculated for each component and service.

## Slide 26: Performance affecting factors
The factors affecting the performance of a computer are:
Heat & Humidity
Magnetism
Stray Electromagnetism
Power Surges
Corrosion & Rough Handling

## Slide 27: Heat & Humidity
Excessive heat and thermal shocks are one of the major factors that effect the performance of the system.
More than half of the power given is wasted as heat and heat destroys the chip
To reduce the heat effect, a fan is installed with the power supply.
The room can be air conditioned.

## Slide 28: …Heat & Humidity
Rapid changes in the temperature result in Thermal Shocks.
Humidity depends on the climate of the place.
It causes short circuiting inside the system and decreases the life of the system.
This factor can be foreseen and air conditioning can be installed as a remedy.

## Slide 29: Stray Electromagnetism
Stray Electromagnetism includes electromagnetism interference, noise, interference, static electricity, etc.
Electromagnetism interference includes cross-talk and radio frequency interference(RFI).
Shielding and isolating system power from other loads is a preventive measure.

## Slide 30: Power Surge
Power surge or fluctuation is a source of lot of problems.
It causes unreliable operation and damages electronic components.
As their bad effects are known in advance, preventive measures should be taken.
Use of uninterrupted power supply (UPS) is a way to safeguard the system.

## Slide 31: Corrosion & Rough Handling
Corrosion of connectors and PCB edge contacts may cause reliability problem in the system.
Moisture is a corrosion agent.
To control Corrosion, humidity should be controlled.
Cleaning fluids should be dried so as to control moisture.

## Slide 32: Rough Handling
Improper handling of the system causes damage.
The system should be kept at a clean and smooth surface.
The system should not be moved from its place frequently.
Careful handling of the system and its peripheral is a simple remedy.

## Slide 33
Basic Computer Maintenance
Clean and Cool
Deleting Temporary Files
Scandisk

## Slide 34
Basic Computer Maintenance
Defragment your Hard Drive
What is Defragmentation?
When you create and delete files and applications on your computer the hard drive will become fragmented.
Data is split into chunks and stored in different areas of the hard disk.
frees up disk space and speeds up your computer.

## Slide 35
Basic Computer Maintenance
How To Defrag Your Harddrive?

## Slide 36
How to Defrag Your Harddrive
  Stop using your computer while you are defragmenting the drive.
  Stop all programs running including your screen saver.
  Run this program overnight
NOTE:

## Slide 37
Basic Computer Maintenance
Hard Disk Error Checking
Uninstall Software
Clean Out Your Recycle Bin
Emptying the Recycle Bin
Operating System Reinstall

## Slide 38
Computer Viruses
What is a virus?
a computer program designed to replicate and spread on its own, preferably without a user’s knowledge
How do viruses spread?
Computer viruses spread whenever infected drives or files are exchanged.
Exchanging computer disks or viewing email attachments.

## Slide 39
How can you protect yourself from viruses?
Computer Viruses
Have an Antivirus program installed on your computer
Regularly scan the computer for viruses (at least once a week).
Keep your virus definition files ,up to date (at least once a month, more times if possible).

## Slide 40
Computer Viruses
Keep updated in regards to the latest security patches for your operating systems and applications
Do not open email attachments that are from people you don’t know

## Slide 41: Thank you